## Slide 1: Metrology Automation Lunch & Learn Metrology.NET® Station Agent
Michael L. Schwartz

## Slide 2
NCSLI – MII Taxonomy
OOP (Object Oriented Programming) in VB.NET
        .NET Reflection
        Properties and Attributes
        Testing & Running Metrology.NET
Learning Objectives

## Slide 3
Veteran owned business, ex-military metrologist
Core business is software
  Metrology consulting
  Efficiencies through automation
  Turn-key system
Focus on finding the right solution for the customer
  Created Metrology.NET® in 2015
  World’s largest MET/CAL® procedure library
  PS-Cal® power sensor calibration solution - Now Tegam’s Product
  C# web-based asset management system
Acquired Cal Lab Magazine in 2011
About Cal Lab Solutions

## Slide 4: Business is about Efficiency?
Better
Cheaper
Faster
That doesn’t mean less accurate

## Slide 5
A Metrology.NET Station Agent is able to run multiple calibrations at the same time on a single GPIB card. This makes the setup a little more complex than just setting the GPIB address.
Problem Statement

## Slide 6
Setting up a Test Station to Test DMM’s with the Fluke 5730A
Test Case UUT HP 34401A
HP 34401A Test Package – Already Created
VISA Script for AC Voltage – Already Created
Standards Used
Fluke 5730A
Agilent 33250A
4-Wire Short
Software Needed
StationAgent.exe
Metrologynet.dll
MessageService.dll
Microsoft .NET reactive libraries
Drivers
Fluke_5700A_Series.dll
Agilent_33250A.dll
UUT_TPController.dll
UUT_DMM.dll
Testing Requirements

## Slide 7
Station Agent Setup
Station Agent Setup
Copy the Files to C:\_StationAgent
** Deleting Driver Files not being used makes the configuration easier.

## Slide 8
Station Agent Setup
Right Click the StationAgent.exe
Run as administrator to setup

## Slide 9
Station Agent Setup
Click Configure  Station Config
Set URL / Login & Password Set Mode to Metrology.NET

## Slide 10
Station Agent Setup
Click File  Local Agent  Start
You may need to open the Firewall Localhost Port 13212

## Slide 11
Metrology MII Taxonomy
URL http://miiknowledge.wikidot.com/start https://www.metrology.net/home/metrology-taxonomy/

## Slide 12
Station Agent Setup
Setting up a Test Station to Test DMMs with the Fluke 5730A
Test Process
Fluke 5730A
TestProcess.Source.Current.AC.Sinewave TestProcess.Source.Current.DC TestProcess.Source.Resistance TestProcess.Source.Voltage.AC.Sinewave TestProcess.Source.Voltage.DC Agilent 33250A
TestProcess.Source.Frequency UUT_DMM
TestProcess.Source.Short.DMM
UUT
UUT_TpController.UUTMeasureVisaScriptControl

## Slide 13
Driver Overview
I/O
Test Process  Source  Instrument
UUTs are Interchangeable

## Slide 14
Station Agent Setup
Click Configure  Add Instrument
Scroll Down to the Fluke_5700A_Series
Press Add

## Slide 15
Station Agent Setup
Expand the Instrument Drivers
Select Fluke_5700A_Series.Driver
Set the Required information

## Slide 16
Station Agent Setup
Repeat for the Agilent_33250A.Driver and UUT_TpControl.UUTMeasure.VisaScriptControl

## Slide 17
Station Agent Setup
Station Configuration should look something like this.

## Slide 18
Driver Overview
I/O
Test Process  Source  Instrument
UUTs are Interchangeable

## Slide 19
Station Agent Setup
Click Configure  Add Driver
Scroll Down to the Fluke_5700A…SourceCurrentAC
Press Add
cc

## Slide 20
Station Agent Setup
Repeat for the Following:
Agilent_33250A.SourceVoltageAC Fluke_5700A_Series.SourceCurrentDC Fluke_5700A_Series.SourceCurrentAC
Fluke_5700A_Series.Resistance4Wire
Fluke_5700A_Series.VoltageAC
Fluke_5700A_Series.VoltageDC

## Slide 21
Driver Overview
I/O
Test Process  Source  Instrument
UUTs are Interchangeable

## Slide 22
Station Agent Setup
Click Configure  Add Test Process
Scroll Down to Fluke_5700A…SourceCurrentACSinewave
Press Add

## Slide 23
Station Agent Setup
Repeat for the following:
Agilent_33250A.TestProcessSourceFrequency Fluke_5700A_Series.TestProcessSourceCurrentDC Fluke_5700A_Series.TestProcessSourceCurrentAC
Fluke_5700A_Series.TestProcessResistance
Fluke_5700A_Series.TestProcessVoltageACSinewave
Fluke_5700A_Series.TestProcessVoltageDC
UUT_DMM.TestProcessSourceShortDMM

## Slide 24
Driver Overview
I/O
Test Process  Source  Instrument
UUTs are Interchangeable

## Slide 25
Running the Automation

## Slide 26
Under the Hood

## Slide 27
Driver Overview
I/O
Test Process  Source  Instrument
UUTs are Interchangeable
Power of OOP

## Slide 28
Under the Hood
UI Auto Writes
Editable
Lists
LimitedToList
Etc…

## Slide 29
NCSLI – MII Taxonomy
OOP (Object Oriented Programming) in VB.NET
        .NET Reflection
        Properties and Attributes
        Testing & Running Metrology.NET
Learning Objectives

## Slide 30: Questions? / Comments
Michael L. Schwartz
Cal Lab Solutions
mschwartz@callabsolutions.com

## Slide 31
Station Agent Setup
Click Configure  Add Instrument
Scroll Down to the Fluke_5700A_Series
Press Add